## Slide 1: Evaluating High-Voltage Battery Performance in the BMW i3 (60 Ah)
Group 8
2024/12/17

## Slide 2: Project Overview
Objective
  Analyze real-world data to predict and optimize battery performance by focusing on:
    Environmental factors
    Vehicle dynamics
    Heating circuit efficiency
Related Variables
  Key Features
    Environmental Data: Temperature, Elevation
    Vehicle Data: Speed, Throttle Position
    Heating Circuit Data: Indoor Temp, Heating Power
  Target Outcome: Predict the State of Charge (SoC) Difference (Battery Consumption)
Approach
  Data Preprocessing: Cleaning and transforming features for modeling
  Modeling: Use Linear Models and Tree-Based Models
  Performance Comparison: Evaluate models for actionable insights

## Slide 3: Model Performance Summary
Linear Models
  Linear Regression: Training MSE = 0.0004 | Test MSE = 0.0006 | R² = 0.7768
  Lasso Regression: Training MSE = 0.0014 | Test MSE = 0.0003 | R² = 0.8797
  Ridge Regression: Training MSE = 0.0005 | Test MSE = 0.0004 | R² = 0.8644
Tree-Based Models
  Decision Tree:
    Training MSE = 0.0000 | Test MSE = 0.0064 | R² = -0.4816
    Feature Importance: Distance [km] = 0.924999
  Random Forest:
    Training MSE = 0.0002 | Test MSE = 0.0018 | R² = 0.5764
    Feature Importance: Distance [km] = 0.816695
Key Insights
  Linear Methods clearly outperform tree-based methods: Lower Test MSE (< 0.0006) and higher R² (> 77%)
  Data exhibits strong linear relationships between predictors and response
  Distance is the most influential feature in both model types, aligning with theoretical expectations

## Slide 4: Analysis Results Summary
SOC Variability:
  The chart (on the left) shows that the variable of interest, SOC, has significant variations, allowing for a meaningful prediction exercise using the features available in the data.
Distance and SOC Relationship:
  The chart (second from the left) demonstrates a linear relationship between distance and battery consumption, with each additional mile requiring a similar amount of energy (SOC/km). This supports the earlier finding that linear models outperform tree-based models, with distance being the most important feature (0.92 feature importance).
Duration's Limited Importance:
  Finally, while trip duration should influence SOC, feature importance analysis (second from the right) shows its importance is minimal (0.02). This is due to high correlation between distance and duration, with distance already capturing most of the relationship with SOC (importance > 0.92, the right one).

## Slide 5
Acknowledgment of Team Members - Group 8
Daniel I Lin
UID: 121033345
Email: dlin0315@umd.edu
Hao-Lin Chiang
UID: 121166357
Email: beas28@umd.edu
Yang-Shun Lin
UID: 121287762
Email: yslin227@umd.edu
Sheng-Hsiang Huang
UID: 121303554
Email: shhuang@umd.edu
Alexios C Papazoglou
UID: 121332967
Email: apapazog@umd.edu
Kai-Wei Hsu
UID: 121366191
Email: kwhsu@umd.edu
Thank you for your attention!
Group 8 - University of Maryland